## Slide 1: Physics-Inspired Distributed Radio Map Estimation
Jan 17, 2025
Dong Yang, Yue Wang
  Computer Science
  Georgia State University, Atlanta, GA, USA

## Slide 2: Outline
Background
Problem formulation
State-of-the-art methods
Our method
Next plan

## Slide 3: What is radio map
Radio map: radio power as a function of location x, frequency 𝑓 and/or with time 𝑡 denoted by
2-D Spatial Space
Frequency
2-D Spatial Space
Time Slots
2-D Spatial Space
3-D Spatial Space
  useful for downstream tasks: network management, coverage planning, spectrum allocation
Radiomap: https://web.altair.com/winprop-telecom
Notes: Network management: detect signal blind or interference and take remedial action
Spectrum allocation: Identify interference areas in the radio frequency band to avoid frequency conflict or overlap

## Slide 4: Problem formulation: Spatial Distribution of Received PSD
  The received PSD can be expressed as:
Full-scale RME
: the transmit PSD of the m-th transmitter at frequencies
: the channel frequency response between the m-th transmitter and a sensor positioned at a location
: the additive white Gaussian noise at location x and frequency f
Received PSD
F
The element of an tensor

## Slide 5: Problem formulation: Radio map estimation (RME)
Learning-based (centralized) RME Romero –Kim’2022
: ground-truth radio map
Sparse measurements
(.)
Building info
Mapping (e.g. DNN)
Full-scale RME
  Measurements: sparse samples collected by terminal devices/sensors
  No channel information required; whereas ray tracing needs channel models
  RUs make partial observations of the global radio map

## Slide 6: Model-based SP method: LDPL[1]
LDPL model:
Making a parameterized version of a., and assuming only 1 TX and the location of that TX is known:
the unknown (, ) of b. can be solved with the aquations (3),(4),(5):
LDPL [1]: Using a Log Distance Path Loss Model based Interpolation method
M. Lee and D. Han, ”Voronoi tessellation based interpolation method for wi-fi radio map construction,” in IEEE Communications Letters, vol. 16, no. 3, pp. 404-407, Mar. 2012.
(1)
(2)
(3)
(4) (5)
where P(d), , P(d0) denote an estimated RSS at distance d from TX to point, path loss, observed RSS at reference distance d0
[1]
Notes: r_i measures i-th error between observed and pred. w_i is a weighting factor for r_i. let r_i have a different level of importance in the sum.
s_i​ represents the RSS at observed point
Locations with a high RSS will have a smaller weight w_i, making them less influential in the optimization.
The parameter p controls the sensitivity of this weighting. Higher p values would give less weight to locations with strong signals

## Slide 7: Model-based SP method: IDW[2]
Estimated RSS are calculated by the sum of observed RSS multiplied by a normalized weight :
Weight wi is calculated by Euclidean distance:
IDW [2]: Using Inverse Weight Model based Interpolation method
S. -P. Kuo and Y. -C. Tseng, “Discriminant minimization search for largescale rf-based localization systems,” in IEEE Transactions on Mobile Computing, vol. 10, no. 2, pp. 291-304, Feb. 2011.
(1)
(2)
where li is the i-th observed point, vi is the observed RSS from TX at the observed point
where l is the location of estimated point, is system parameter (typically =0.01)
Limitation of Model-based SP method:
Not capturing shadowing effects (buildings)
[2]

## Slide 8: Generative AI with Physics Loss for RME[3]
Unlike Image Recovery
Spectrum coverage follows physical radio propagation principles.
RME-GAN [3]: Customize the physical loss function of conditional GAN for radiomap estimation
S. Zhang, A. Wijesinghe, and Z. Ding, “Rme-gan: A learning framework for radio map estimation based on conditional generative adversarial network,” IEEE Internet of Things Journal, vol. 10, no. 20, pp. 18 016–18 027, 2023
[3]

## Slide 9: Overall Framework of RME-GAN
S. Zhang, A. Wijesinghe, and Z. Ding, “Rme-gan: A learning framework for radio map estimation based on conditional generative adversarial network,” IEEE Internet of Things Journal, vol. 10, no. 20, pp. 18 016–18 027, 2023
[3]
Notes: Epsilon
Brightness similarity
Contrast similarity
structural

## Slide 10: Simulation Results
S. Zhang, A. Wijesinghe, and Z. Ding, “Rme-gan: A learning framework for radio map estimation based on conditional generative adversarial network,” IEEE Internet of Things Journal, vol. 10, no. 20, pp. 18 016–18 027, 2023
[3]

## Slide 11: Federated Learning for distributed RME [4]
Local input:
  Local sensor sparse RSS
  Sensor mask
  City map
Homogeneous local tasks: RME given sparse sensor data and building info.
Allow overlapping between adjacent regions.
Combine trimmed local outputs for global RME.
Weishan Zhang, Yue Wang, Lingjia Liu, Zhi Tian, “FedRME: Federated Learning for Enhanced Distributed Radiomap Estimation,” in 2024 IEEE 100th Vehicular Technology Conference (VTC2024-fall). IEEE, 2024.
[4]
Notes: In realistic scenarios, a centralized fusion center consumes a huge amount of communication resource in processing raw data and aggregating spectral measurements from all sensor devices, which also raises critical concerns on data privacy leakage

## Slide 12: Simulation Results
Trained with sufficient training data (20k training)
Trained with limited training data (1k training)
RMSE vs sensor volume (1000 testing instances)
Comparable RMSE to centralized learning
Outperforming the standalone method.
Apparently outperforms all baselines

## Slide 13: Simulation
Fewer
sensors
More
sensors
Example output of different RME methods (1k training data):
FedRME gives more reasonable estimates, especially around the Tx
Notes: Due to overfitting, cannot find source
Stdaln:

## Slide 14: Physics-inspired distributed RME: Challenge
Challenge: Heterogeneous local tasks: RME only given sparse sensor data and TX location.
Notes: Due to the impact of buildings, the channel condition is inconsistent over space, results in heterogeneous local data/tasks.
There is always a discrepancy across clients.
This is due to the unique building distributions in local environments among clients.

## Slide 15: Physics-inspired distributed RME: Motivation
Received Signal Power (dB) =free space path loss + shadow fading + Rayleigh fading
Notes: To address such model heterogeneity among clients, inspired by the domain knowledge that different wireless channel models hold different propagation properties leading to different impacts on received signal power,

## Slide 16: Designing model
Received Signal Power (dB) =free space path loss + shadow fading
Common part for each client for FL
Individual part for each client for FL
Client i
Input: Measurements, Tx location
Output: Estimated radio map
Notes: we decouple the entire deep learning model into different modules.
It allows clients to collaborate in training their common module to capture the pathloss influence, and meanwhile, to train their client specific module individually.

## Slide 17
Client 1
…
Client S
pull
push
Anchor
Positive
Negative
Weighted Constraint Regularization
=

## Slide 18: Loss function for common representation: Gradient Smoothness
Getting the gradients for each grid:
Gradient-based loss function:

## Slide 19: Loss function for common representation: Weighted constraint regularization
Round z-1
Round z
Round z+1
Epoch 1… T
Notes: Different wireless channel models exhibit distinct propagation properties, thus to mitigate potential biases in local radio propagation,
We propose this to guide g^s_com in learning common propagation features.

## Slide 20: Loss Function for Individual representation
Where
Loss function for recovering individual radio maps:

## Slide 21: Dataset: RadiomapSeer[4]
Client 1
Client 2
Client 9
…
1
2
80
…
…
“OpenStreetMap contributors.” Planet Dump. 2017. [Online]. Available: https://planet.osm.org
[4]
Notes: Cellular network
The radio maps are stored as 2D grids of size 256 × 256 m2, with a spatial resolution of 1m per grid cell
Suppose each client only monitors one region.

## Slide 22: Training Cases
Data augmentation
256
256
49
32
…
The 256×256-size radio map
49 smaller radio maps of size 64×64
Three different cases
Case-1: uniformly sample. 12.5% of sparse measurements;
Case-2: a random rate. between 1% and 10% for each client;
Case-3: an unbalanced manner. 1% rate on one half and 10% on the other half.
Notes: In this way, each client has access to 80 radio maps. Overfitting
To mitigate this issue, we apply data augmentation by dividing each 256×256-size radio map into 49 smaller radio maps of size 64×64, with an overlap of 32 grid cells between adjacent radio maps.

## Slide 23: Result: Visualization
The proposed method appear in higher quality and more closely resemble to the true map

## Slide 24: Result：Visualization(consistency)
True RM
Learned Common part
Client 7
Client 7
Client 7
Client 7
The work can learn the common parts over clients
Free space path loss
Physical meaning

## Slide 25: Next Plan –Schedule
1/17—4/30
Complete the paper and submit it for Journal publication
5/1—5/31
Design RME without TX location and city maps / decentralized learning for distributed learning
6/1—6/30
Writing papers and model parameters tuning
7/1—7/31
Optimize paper script
Complete the paper and submit it for Conf./Journal publication

## Slide 26: Next Plan – Algorithm Level
Federated learning ->Decentralized learning RME
  Consensus-based collaborations via ADMM
  Hierarchical hyper-graph learning based on wireless network topology, devices capability, link resource, and data availability
Compressed sensing and hybrid NN training
  Domain knowledge: statistics, basis, structures
  Sparse representation and dictionary learning
known basis
unknown coefficients
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1
1

## Slide 27
Thank You!