## Slide 1: Semantic Communication: Fundamentals, Challenges and Future Directions
Presenter: Ziyang Wei
04/18/2025
1
1

## Slide 2: Outline
Introduction
Technical Approaches
Security Challenges
Future Directions
Conclusion
2

## Slide 3: Introduction Technical Approaches Security Challenges Future Directions Conclusion
3

## Slide 4: Motivation
Limitations of Traditional Communication
  Focuses on bit-level transmission accuracy.
  Semantic meaning is not considered in system design.
  Semantic understanding depends on context and shared knowledge.
4
Z. Lu et al., "Semantics-Empowered Communications: A Tutorial-Cum-Survey," in IEEE Communications Surveys & Tutorials, vol. 26, no. 1, pp. 41-79, Firstquarter 2024

## Slide 5: What is Semantic Communication?
Semantic Communication (SemCom) refers to the process of transmitting meaningful information between transmitter and receiver.
  Encoder extracts semantic features (images → feature vectors).
  Feature vectors transmitted over a communication channel.
  Decoder reconstructs the original information.
5
W. Yang et al., "Semantic Communications for Future Internet: Fundamentals, Applications, and Challenges," in IEEE Communications Surveys & Tutorials, vol. 25, no. 1, pp. 213-250, Firstquarter 2023
Notes: Do not transmit all original data, discard redundant data, and only transmit key information that can completely restore the original data.Since semantic communication transmits key information instead of all data, the bandwidth requirement is much lower than traditional communication.

## Slide 6: Introduction Technical Approaches Security Challenges Future Directions Conclusion
6

## Slide 7: Technical Approaches
Classical Semantic Information Theory
Knowledge Graph-Based Communication
Deep Learning-Based Approaches
Goal-Oriented Communication
7

## Slide 8: Classical Semantic Information Theory
To extend Shannon's theory to include the meaning of information, not just its symbols. semantic entropy:
  ,
  : a semantic unit, : probability of meaning
Semantic Mutual Information
  , If the transmitter and the receiver have more consistent "semantics" for the same message, the higher the mutual information.
8
Z. Lu et al., "Semantics-Empowered Communications: A Tutorial-Cum-Survey," in IEEE Communications Surveys & Tutorials, vol. 26, no. 1, pp. 41-79, Firstquarter 2024

## Slide 9: Knowledge Graph-Based Semantic Communication
Knowledge Graph (KG): structured graph of entities and relations.
A graph-based semantic structure: , V: nodes = entities/concepts, E: edges = semantic relations
  Encoder extracts semantic triplets, e.g.:(dog, is-a, animal)
  Receiver reconstructs meaning using shared Knowledge Base.
9
Z. Lu et al., "Semantics-Empowered Communications: A Tutorial-Cum-Survey," in IEEE Communications Surveys & Tutorials, vol. 26, no. 1, pp. 41-79, Firstquarter 2024

## Slide 10: Deep Learning-Based Semantic Communication
Core Idea: Use neural networks to extract, compress, and reconstruct semantic representations from raw data.
Autoencoder-style structure:
10

## Slide 11: Goal-Oriented Semantic Communication
Core Idea
  Transmit only the semantic content relevant to a specific goal or task.
  Receiver does not reconstruct full message — only needs to complete task.
Challenges:
  Hard to generalize across tasks.
  Requires precise goal definition.
11
T. M. Getu, G. Kaddoum and M. Bennis, "A Survey on Goal-Oriented Semantic Communication: Techniques, Challenges, and Future Directions," in IEEE Access

## Slide 12: Introduction Technical Approaches Security Challenges Future Directions Conclusion
12

## Slide 13: Security Challenges in Semantic Communication
Semantic Adversarial Attacks
  Craft inputs that result in incorrect semantic decoding (similar to adversarial examples in vision/NLP).
Knowledge Base Manipulation
  Modify or inject false facts into shared semantic knowledge.
Model Stealing
  Reverse-engineering of encoder/decoder functionality from intercepted samples
13
Slightly altering text/image → changes meaning
Apple is a vegetable
M. Shen et al., "Secure Semantic Communications: Challenges, Approaches, and Opportunities," in IEEE Network, vol. 38, no. 4, pp. 197-206, July 2024

## Slide 14: Defense Strategies and Open Security Problems
Knowledge Base Attacks
  Graph consistency checking-Avoiding injection of fake semantic facts into the shared KG
  Access control-Restrict who can read/write to semantic knowledge sources
Semantic Adversarial Attacks
  Adversarial training-Training the encoder with perturbed inputs to resist semantic confusion
  Semantic denoising
Model Parameter Inference
  Gradient/Parameter Encryption(FL)
14
M. Shen et al., "Secure Semantic Communications: Challenges, Approaches, and Opportunities," in IEEE Network, vol. 38, no. 4, pp. 197-206, July 2024

## Slide 15: Introduction Technical Approaches Security Challenges Future Directions Conclusion
15

## Slide 16: Future Directions
Multimodal Semantic Communication
  Most current research focuses on a single modality (text/image).
  Future systems need to support multimodal input (e.g., text, speech, action).
  How to achieve multimodal semantic alignment.
Semantic Integrity Verification
  Semantic correctness or task-aligned meaning needs to be defined.
  At present, there is a lack of mechanisms to verify whether "semantics are destroyed".
16

## Slide 17: Introduction Technical Approaches Security Challenges Future Directions Conclusion
17

## Slide 18: Conclusion
The motivation for Semantic Communication
Core definitions, system architecture, and technical paths
Security threats & defenses in semantic-level systems
Future challenges
18

## Slide 19: Reference
W. Yang et al., "Semantic Communications for Future Internet: Fundamentals, Applications, and Challenges," in IEEE Communications Surveys & Tutorials, vol. 25, no. 1, pp. 213-250, Firstquarter 2023
D. Wheeler and B. Natarajan, "Engineering Semantic Communication: A Survey," in IEEE Access, vol. 11, pp. 13965-13995
M. Shen et al., "Secure Semantic Communications: Challenges, Approaches, and Opportunities," in IEEE Network, vol. 38, no. 4, pp. 197-206, July 2024
T. M. Getu, G. Kaddoum and M. Bennis, "A Survey on Goal-Oriented Semantic Communication: Techniques, Challenges, and Future Directions," in IEEE Access
Z. Lu et al., "Semantics-Empowered Communications: A Tutorial-Cum-Survey," in IEEE Communications Surveys & Tutorials, vol. 26, no. 1, pp. 41-79, Firstquarter 2024
29

## Slide 20: Thank you!
20